JININ ELECTRET CONDENSER MICROPHONE UNITS

| MODEL EM-6022P OMNI DIRECTIONAL |
| --- |
| SENSITIVITY (O dB=1V/bar,1KHz, VCC=2V, RL=2.2KΩ) -38±2dB -40±2dB -42±3dB -44±3dB -46±3dB | CIRCUIT DIAGRAM |
| SPECIFICATIONS IMPEDANCE：Less than 2.2KΩ STANDARD VOLTAGE：2.V RANGE OF OPERATING VOLTAGE：1.5V TO 10V CURRENT DRAIN：0.5mA MAX S/N RATIO：58 dB or more MAXIMUM INPUT SOUND PRESSURE：120 dB SPL RoHS Compliant. |
| 4. DIMENSION |
| 5. TYPICAL FREQUENCY RESPONSE CURVE |

| 6. RELIABILITY TEST |
| --- |
|  | VIBRATION TEST | TO BE NO INTERFERENCE IN OPERATION AFTER VIBRATION 12Hz TO 50Hz FOR 1 MINUTE FULL AMPLITUDE, FOR 1.5 HOUR AT 3 AXISES. |  |
|  | DROP TEST | TO BE NO INTERFERENCE IN OPERATION AFTER DROPPED TO CONCERTET FLOOR EACH ONE TIME FROM 1 METER HEIGHT AT 3 DIRECTONS IN STATE OF PACKING. |  |
|  | TEMPERATURE TEST | AFTER EXPOSURE AT 55° FOR 1 HOUR, SENSITIVITY TO BE WITHIN +/-3dB FROM INITIAL. AFTER EXPOSURE AT -10° FOR 1 HOUR, SENSITIVITY TO BE WITHIN +/-3dB FROM INITIAL. (THE MEASUREMENT TO BE DONE AFTER 2 HOURS OF CONDITIONING AT 25°C.) |  |
|  | HUMIDITY TEST | AFTER EXPOSURE AT 40°C AND 95% RH FOR 48 HOURS, SENSITIVITY TO BE WITHIN +/-3dB FROM INITIAL. (AFTER 1 HOUR OF CONDITIONING AT 25°C.) |  |
|  | TEMPERATURE CYCLE TEST | AFTER EXPOSURE AT -10°C FOR 1HOUR, AT 25°C FOR 1 HOUR, AT 50°C FOR 1 HOUR, ATO 25°C FOR 2 HOURS, 4 CYCLES ,SENSITIVITY TO BE WITHIN +/-3dB. (AFTER 2 HOURS OF CONDITIONING AT 25°C) |  |
| *REGARDING THE SOLDERING OPERATION： EACH CONDENSER MICROPHONE CONTAINS A FET WITHIN ITS CASE. GENERALLY, OVER-HEATING, OVER-CHARGE OF VOLTAGE IS EASY TO DESTROY SEMICONDUCTORS. USE 30W (OR UNDER) SOLDERING IRON AND MAINTAIN 230°~260°C IN OPERATION. SOLDERING SHOULD BE ACCOMPLISHED WITHIN TWO SECONDS AT EACH TERMINAL SO AS NOT TO BE OVERHEATED. DO NOT MAKE A CAVITY AT THE SERFACE OF LEAD ON THE PATTERN PLATE. (A CAVITY MAY CHANGE THE CHARACTERISTICE OF CONDENSER MICROPHONE.) |

JIN IN ELECTRONICE CO., LTD

5F., NO 5-1, BAO HORNG RD., HSIN TIEN CITY ,TAIPEI, TAIWAN

TEL:886-2-29128689

FAX:886-2-29115517